RecyCREATE with glass bottles

Abat-jour project

Materials:

- N° 1 Glass bottle

- N° 1 Lampshade

- N° 2 mt Bipolar electric cable (1 mmq)

- N° 1 Electric plug 10 Ampere

- N° 1 Electric Switch per Paralume

- N° 1 Bulb socket

- N° 1 Lamp

- Bi-component glue

Tolls:

- Drill

- Glass drill bit

- Protective gloves

- Protective glasses

- Various tolls

The principal activity is to realize the hole in the glass bottle. To do it we must use a column drill for a best stability and accuracy and a glass drill bit (called lance bit). The lance bit have to refrigerate during the drilling phase. Very, very important - During the drilling of the bottle you must dress protective glass and gloves. With one hand you keep hold the bottle, with the other hand you use the drill. Keep calm and perforate the bottle in little step, don’t force the lance bit. You can practice before you start. After the perforation you must clean the hole on the bottle and you must insert the electric cable. To one end you will connect the electric plug, in the middle of the cable you will install the electric switch and to the other end you will connect the bulb socket. Fixing of the bulb socket and the lampshade to the bottle depend by the type of neck of the bottle, to do it you can use the bi-component glue or (if you are lucky!) the thread collar of the bulb socket.

The work can be concluded, but for all the activity like this your fantasy or one your idea or necessity can add to the abat-jour some other solutions. By the way you will realize one original abat-jour with one bottle and few euro!

www.ricicreare.it – info@ricicreare.it

# Text boxes

www.ricicreare.it